## Slide 1: Cascaded polyphase filter banks #2
Oversampled cosine-modulated filter banks

## Slide 2: Oversampled Modulated Filter Banks
Literature
  S. Weiss, Analysis and Fast Implementation of Oversampled Modulated Filter Banks. In John G McWhirter and Ian K. Proudler (eds.): Mathematics in Signal Processing V, IMA, pp.263-274, 2001.
  S. Weiss and R.W. Stewart, Fast Implementation of Oversampled Modulated Filter Banks. IEE Electronics Letters, Vol.36(No.17): pp.1502-1503, August 2000.
  S. Weiss and R.W. Stewart, On Adaptive Filtering in Oversampled Subbands. Volume 8 in series: Berichte aus der Kommunikations- und Informationstechnik (eds. B. Girod and J. Huber). Shaker Verlag, Aachen, 1998 (ISBN 3-8265-4566-4), 213 pages.
http://www.ecs.soton.ac.uk/~sw1/software/software.html
This work is based on:

## Slide 3: Cascaded filter-bank with oversampling – basic idea
Combined second-stage outputs contain no first-stage aliasing and no gaps
frequency
First-stage sub-band is oversampled, so no aliasing occurs
Nyquist band
Nyquist band
Band k
Band k+1
frequency
frequency
Overlap prevents gap
Only the alias-free colored areas are used after second-stage filtering

## Slide 4: Cascaded filter-bank with oversampling - schematic
Filter bank 1
Fbank 2
Fbank 2
Fbank 2
Fbank 2
Fbank 2
Fbank 2
Fbank 2
Fbank 2

## Slide 5: Example
In the following example, the first stage is a real 8-band cosine-modulated filter bank, and the second stage is a 16-band complex cosine-modulated filter-bank
All filter-banks are 16/14-fold oversampled

## Slide 6: First-stage real filter-bank frequency sweep

## Slide 7: Second-stage complex filter-bank frequency sweep

## Slide 8: Cascaded oversampled filter-bank (chirp-)sweep output, first-stage aliasing eliminated

## Slide 9: Preliminary conclusions
The cascaded oversampled cosine-modulated filter bank principle seems to be successful in eliminating the first-stage sub-band aliasing
The computational costs are somewhat higher than those of the critically-sampled polyphase filter banks:
  The first stage includes a complex FFT, as compared to a real FFT for the polyphase filter banks
  Complex modulation is added
  The oversampling procedure requires a more complex buffering structure

## Slide 10: Polyphase FIR / FFT filter-bank
z -1
x(n)
M-point FFT
h0
z -1
z -1
z -1
z -1
z -1
+
+
+
+
z -1
z -1
z -1
z -1
+
+
+
+
z -1
z -1
z -1
+
+
+
+
z -1
h1
h2
hM-1
hM
hM+1
hM+2
h2M-1
h2M
h2M+1
h2M+2
h3M-1
hNM-1
h(N-1)M
h(N-1)M+1
M
M
M
M
h(N-1)M+2

## Slide 11: Oversampled modulated polyphase filter-bank
z -1
x(n)
Transform T
h0
z -1
z -1
z -1
z -1
z -1
+
+
+
+
z -1
z -1
z -1
z -1
+
+
+
+
z -1
z -1
z -1
+
+
+
+
z -1
h1
h2
hK-1
hK
hK+1
hK+2
h2K-1
h2K
h2K+1
h2K+2
h3K-1
hLK-1
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
N
h(L-1)K+1
h(L-1)K+2
h(L-1)K

## Slide 12: Real modulated polyphase filter-bank (first stage)
z -1
x(n)
Transform T
h0
z -1
z -1
z -1
z -1
z -1
+
+
+
+
z -1
z -1
+
z -1
z -1
+
+
+
+
z -1
h1
h2
hK-1
hK
hK+1
hK+2
h2K-1
h2K
h2K+1
hLK-1
N
N
N
N
N
N
N
N
N
N
N
N
N
h(L-1)K+1
h(L-1)K+2
h(L-1)K
×
×
×
×
K-point IDFT
×
×
×
×
z -1
+
N
discarded
Real numbers
complex numbers
complex modulation
Fs (real) samples/second
Fs/N samples/second
K/2 complex outputs
real filter coefficients hk
This is not a set of K FIR filters! Because of the oversampling, individual input samples appear in different rows during the processing

## Slide 13: Another example: 128672 bands
First stage filter bank:
  Real inputs
  K1=256 ; M1=128 sub-bands
  Decimation factor N1=224
Second stage filter banks:
  M1=128 filter-banks, one for each first-stage output sub-band
  These filter banks are the complex version of the first-stage filter-bank:
    K2=256 ; M2=256 sub-bands
    Decimation factor N2=224
    K2*(N1/K1)=224 of the K2=256 output bands are used; the other K2*(K1- N1)/K1=32 are discarded
Total # output bands = M1* K2*(N1/K1)= N1*K2/2=28672

## Slide 14: 28672-bands cascaded filter bank
Matlab refuses to make a spectrogram of 28672 frequency bands (too much information for Matlab to plot)
In the following plot a chirp frequency sweep is shown over the first 1800 second-stage output sub-bands (a little bit over 8 first-stage output bands)

## Slide 15: Cascaded oversampled filter-bank (chirp-)sweep output, 28672-bands example

## Slide 16: Full sweep
A sweep over the whole range from 0 to  was also made successfully but can not be shown here
A part of the sweep is shown in the following slide

## Slide 17: Cascaded oversampled filter-bank (chirp-)sweep output, 28672-bands example, partial plot (bands 16000-19000)

## Slide 18: Prototype frequency response

## Slide 19: Residual aliasing
Some aliasing is still remaining
The following plots show the sub-band outputs with a sine-wave input
The maximum aliasing level is about 30 dB below the signal level (in this test case)
Some work remains to be done in optimizing the prototype further; for example increase the oversample ratio (this is 256/224=1.143 in this example)

## Slide 20: Aliasing levels of 128*224-band cascaded filter bank

## Slide 21: Aliasing levels of 128*224-band cascaded filter bank, first 5000 outputs

## Slide 22: Higher oversampling ratio gives better alias rejection
Increasing the oversampling ratio to 256/208 (=16/13=1.231) improves the aliasing suppression
In the following example aliasing is 58 dB below the signal
First stage filter bank:
  Real inputs
  K1=256 ; M1=128 sub-bands
  Decimation factor N1=208
Second stage filter banks:
  M1=128 filter-banks, one for each first-stage output sub-band
  These filter banks are the complex version of the first-stage filter-bank:
    K2=256 ; M2=256 sub-bands
    Decimation factor N2=208
    K2*(N1/K1)=208 of the K2=256 output bands are used; the other K2*(K1- N1)/K1=48 are discarded
Total # output bands = M1* K2*(N1/K1)= N1*K2/2=26624

## Slide 23: Cascaded oversampled filter-bank (chirp-)sweep output, 128*208=26624-bands example

## Slide 24: Aliasing levels of 128*208-band cascaded filter bank

## Slide 25: Aliasing levels of 128*208-band cascaded filter bank, first 5000 outputs