## Slide 1: Filter bank requirements and design issues

## Slide 2: Filter requirements 1st filter-bank
Filter quality | Value | Filter design | Value
Stop-band attenuation | > 75 dB | Prototype filter length | 4096
Pass-band ripple | < 0.01 % | Number of sub-bands | 128
Stop-band ripple | < 0.1 % | Filter window type | fircls
Transition band | < 3 kHz | Pre-filter length | 16
Temporal depth | < 0.2 ms | Decimation factor (critical sampling) | 128
Bandwidth ratio | 1 / 128 |  | 
From: LOFAR Architectural Design Document, Rev. 3.0

## Slide 3: Assumptions so far:
The filter-bank is implemented as a polyphase DFT filter bank
A prototype low-pass FIR filter is designed first length L (in our case L=4096)
The response of the prototype is frequency-shifted by multiplying in an M-point FFT with
M = 2 * #bands = 2 * 128 = 256
The filter bank consists of M polyphase filters of length N=L/M (in our case: N=16) followed by an M point FFT
The computational complexity is roughly that of a length-L FIR filter + an M-point FFT

## Slide 4: Problems with current assumptions vs. requirements
With L=4096, the transition band  40 kHz, not 3 kHz
For transition band 3 kHz, L should be roughly 95000 !
Sub-band aliasing
  since the prototype FIR can never be strictly band-limited (stop-band attenuation   , stop-band ripple  0), decimation results in aliasing of out-of-band (transition-band) signals to in-band frequencies

## Slide 5: FIR filter
z -1
z -1
h(1)
+
z -1
+
z -1
+
h(L-1)
+
z -1
x(n)
y(n)
h(0)
h(2)
h(3)

## Slide 6: Polyphase FIR / FFT filter-bank
z -1
x(n)
z -1
z -1
M
z -1
z -1
z -1
+
z -1
M
z -1
z -1
z -1
+
z -1
M
z -1
z -1
z -1
+
M-point
FFT
z -1
y0(n)
y1(n)
yM-1(n)
h0
h1
hM-1
hM
h2M
h(N-1)M
hM+1
h2M+1
h(N-1)M+1
h2M-1
h3M-1
hNM-1

## Slide 7: Filter bank of 128 4096-taps FIR filters, 40kHz trans.band

## Slide 8: Polyphase filter bank frequency sweep, showing start-up effect

## Slide 9: Polyphase filter bank frequency sweep, start-up effect discarded

## Slide 10: Filter bank response short-comings
In the prototype FIR filter, the transition band is far to wide (40 kHz instead of 3 kHz)
Out-of-band signals, from the (wide) transition bands, alias into the sub-bands because of decimation; alternatively, by making the bands narrower, gaps occur between sub-bands

## Slide 11: How to get a smaller transition band
The transition band of a FIR filter can be reduced, without increase of the computational complexity, by the use of IFIR methods (Interpolated FIR)
  Stretch the frequency response requirements by a factor K (multiply pass-band cut-off frequency and transition-band by factor K)
  Design a FIR filter H(z) meeting these relaxed requirements
  Compress the frequency band (construct H(zK) ) by adding K-1 zeros between successive impulse response coefficients
  Remove the K-1 resulting images of the response around frequencies n*Fs/K by a second filter G(z)
  The filter resulting from cascading H(zK) and G(z) meets the requirements

## Slide 12: Interpolated FIR
stretch K=4 times
design FIR H(z)
freq.
stop-band attenuation
transition band
insert zeros
0
Fs/2
Fs
frequency transfer function of H(zK) and interpolation FIR G(z)
Fs
frequency transfer function of cascade H(zK) G(z)
G(z)
H(z)
H(zK)
image bands

## Slide 13: Interpolated FIR design of prototype filter
With the current ADD requirements in mind, the prototype FIR low-pass filter was designed using the IFIR method
Interpolation factor K=32 was optimal
All requirements were met except temporal depth
H(z32) with 2959 non-zero taps
G(z) with 188 taps
Direct-form realization of total filter H(z32)G(z) in 1 section would have 94844 taps
Temporal depth = 94844 / 64e6 = 1.5 msec (> 0.2 msec)
Two cascaded sections H(z32) and G(z) result in 2959+188=3147 non-zero taps, so arithmetic complexity is reduced by a factor 94844/3147  30 as compared to single-section direct-form implementation

## Slide 14: IFIR implementation of prototype (zoomed in)

## Slide 15: IFIR implementation of prototype (zoomed in 2)

## Slide 16: IFIR implementation of prototype (zoomed in 3)

## Slide 17: IFIR implementation of prototype

## Slide 18: Where do we stand now?
Is our problem solved now? Noooo… not by a long shot
Can we include this IFIR solution in a polyphase-like filter-band structure to reduce complexity? We don’t want to implement 128 separate filters Hk(z32)Gk(z) with a total of 128 x 3147 = 402816 taps
Can we find a polyphase-like structure which eliminates the sub-band aliasing?
Maybe the solution can be found in
  cosine-modulated FIR filters
  QMF (Quadrature Mirror Filter) structures
  pseudo-QMF
  FRM approach (Frequency-Response Masking) ?
  There is a lot of (recently appeared) literature to be found on this topic
Should we resort to IIR filters (and give up linear phase)?