## Slide 1: Filter study : Goals
Find the filter specification, requirements.
Evaluate the unwanted distortion, perturbation once the design of the filter is implemented on a real acquisition chain(ADC non linearity, quantization…)
Installation on Theta, ITS set up

## Slide 2: Filter procedure investigation
Test bench
Design Filter
Initial requirements
Define Implementation evaluation
Evaluate filter
Theta Implementation

## Slide 3: Requirements + Filter design
Filter :
  1st experiment : FIR Low Pass
Filter structure :
  FIR Bank
  Polyphase
  ……
Rp
Tb
Suppression level
Coefficient for the filter

## Slide 4: Test bench
ADC : 80Ms/s
Control Pc
GPIB interface
Ethernet link 100Mb/s
Data Wrapper
Data Unwrapper
FPGA
ADC
Data generator

## Slide 5: 1st Experiment
The purpose is to build the test bench. We will use a very simple set up
Filter set up :
  FIR : Coefficient real
  10 bits for the coefficient
  Rp : 0.5dB, Att : -70dB, Bs, 128khz
Experiment set up :
  FIR : Coefficient real
  Sweeping real sinwave every kHz :
    to evaluate the amplitude of the transfer function of the implemented filter and compare with the theoretical one
    Cosine fitting on the input and output and phase delay evaluation

## Slide 6: Conclusion
Pragmatic approach which allow us a good comprehension of the signal processing
  Sweeping slowly from requirements to usage
  in evaluating difference between theory and implementation
First experiment will allow us implement and verify the test bench