## Slide 1: Measurement effects
12 bits input signals
10 bits input signals
Number of input bits: Influence of the quantized input signal for the tests

## Slide 2: Artefact in the measurements
It is happening every P*Fs/Nfft with P =1….Nfft due to the downsampling operation.

## Slide 3: Test bench experiments
Using Ns input sample: 100000

## Slide 4: Test bench experiments (2)
Using Ns input sample: 400000

## Slide 5: Test bench experiments (3)
Using Ns input sample: 800000

## Slide 6: Filter verification
10 bits
12 bits

## Slide 7: Conclusion: Towards the test bench
The quantization problem we had on the filter was only due to the small number of data point after downsampling. ( Same number of data used for D=32 was OK but since we have now D = 1024, we should increase the number of input points). The fitting algorithm didn’t have enough point to evaluate good phase and amplitude
Take care to have at least more than 500 Points to evaluate the amplitude and phase of the sinewave out of the filter
The artefact of the measurements are happening at fs/Nfft
Change the packet size according to new settings.

## Slide 8: Towards filter bank
Improvements on the filter design is not much we still have:
    Stop band: -90.5dB
    Pass band ripple: -0.45 dB
    -3dB -> 40dB: 23.3%
    -3dB -> 90.5dB: 32.89%
    Bit exact simulation:
    - 2 Truncations
    - after 1st addition: 18 bits
    - after adder tree: 18 bits

## Slide 9: Towards filter bank (2)
  FFT fixed - points
  Model from Wessel (Matlab)
  Quantization study : on the polyphase filter structure + on the FFT
  Usual test + bench
  Documentation:
      Wietse currently writes a document about the implementation fo the polyphase filter bank under VHDL
      Dion comments the Jerome’s document about the theoritical background of the polyphase filter bank. It needs now some rewrittings.
      Jerome has started with a document explaining motivations and design method for the LOFAR test station
  We can already think about the oversampled polyphase filter bank…. Further discussions should start in about 3 weeks to a month…..