## Slide 1: Problematic
The specification of the main processing have changed: 254 -> 1024 channels (200mHz)
therefore we can : 4K -> 16K.
Problematic:
What are the filter characteristic ?
How to generate 16K filter windows ?? the max for Matlab is 5K (5K*5K LSQ method-> memory problems)

## Slide 2: Filter characteristic
Specifications defined and motivated by: A.G, JB, A.J.B, J.D considering Calibration, RFI stakeholder:
    PBRipple: 0.5dB
    SBRipple: 91dB
    Transition Band: 1 subband ( 160/195KHz)
    Decreasing stop band to attenuate far away in the spectrum RFI folding)A document is on progress.

## Slide 3: Filter design
The filter design method fircls1 LSQ based methods gives good result for the basic 2-4K design.
A interpolation should be applied in order to realize 4K -> 16K coefficient generation. (Add 16K coefficients within the 4K coefficients). Two mthod are possible
- Classic: 0 padding + FIR (long if good filter quality)
- FFT : creation of the bandwidth in padding zeros directly in the frequency domain.

## Slide 4: Frequency domain comparison

## Slide 5: Time domain comparison

## Slide 6: FFT Window comparison
FFT method a lot faster than the classic interpolation and gives far better result. The method can be improved in using different windows: trade off are then done on the window shape

## Slide 7: Window comparison

## Slide 8: ModelSim VHDL verification : Gain

## Slide 9: ModelSim VHDL verification :Phase

## Slide 10: Conclusion:
Verify the ModelSim bench result and redo to check the phase
Continue writting documentation
    Theoretical background of digital filtering
    Filter design motivation
    Hardware implementation verification: Test bench
Verify the result on the test bench itself: Only a subbad subset because (40MHz AD and not enough processing power on the current demo board)
Think about a good way to test on the new board delivered in the end of septembre